## Slide 1: Virtual Router
Savan Kiran
Jasmine Dhillon
Bhanu Prakash Meka

## Slide 2: Overview
Enhance Router Security
  By dividing responsibilities
    Control OS (Monitors working of Router OS and helps in detecting attacks and recovering from them)
    Router OS (Handles all the traditional responsibilities of a router)
  Achieve virtualization on a commercial router

## Slide 3: Xen
Architecture (why Xen?)
Source and Compilation (what is Xen?)
Build output (how Xen?)

## Slide 4: Xen - Architecture

## Slide 5: Xen – Architecture contd.
Type-1 hypervisor (Bare metal)
Supports ARM architecture
Control & Data plane virtualization
Advanced interface between Driver and Guest domains
Open source

## Slide 6: Xen - Source
Xen source code has 4 modules
  Xen core
    Main components of xen hypervisor – dom0, domU and driver stubs
  Tools
    Xen command line tools and interface between dom0 and domUs
  Stubdom
    (Extended feature) Instead of keeping all hardware drivers in dom0, move them to a separate stubdom for security reasons
  Docs
    Manual pages & other documents for Xen

## Slide 7: Xen - Compilation
ARM cross-compilation
  Necessary as the target hardware is different from host
  Create a sandboxed environment
    Using ‘sbuild’ and ‘schroot’
    Install ARM32-eabi-hf toolchain
  Compile Xen inside the sandbox
    make dist CROSS_COMPILE=arm-linux-gnueabihf- XEN_TARGET_ARCH=arm32

## Slide 8: Xen – Build output
Xen binaries
Xen config files
  Can modify to adapt Xen to the hardware before actually installing Xen
Xen init scripts
  Can modify to match the right boot sequence between Xen components and dom0
Xen libraries
  Libraries necessary for Xen to work
Xen docs

## Slide 9: Netgear Nighthawk R7000 router

## Slide 10: Netgear R7000 - Specification
CPU
  Broadcom BCM4709A0 ARMv7 1GHz 2 core processor
  Doesn’t support hardware virtualization
    However, Xen supports para-virtualization
Memory
  256 MB
Flash
  128 MB
  Stock DD-WRT image is ~20 MB
  Xen compiled is ~7 MB
  Sufficient space left for a DomU
Filesystem
  Squash FS – Compressed, Read-only

## Slide 11: Netgear R7000 – Specification contd.
Bootloader
  Common Firmware Environment (CFE)
  Written by Broadcom
  Made open source recently
  Has extended features to flash and control how a system boots
Serial Communication
  Via USB-TTL (UART) cable
  Allows to interact with the bootloader and observe boot sequence
Stock OS
  DD-WRT (Linux based)
  But provides no device-tree which Xen requires to understand the hardware

## Slide 12: Netgear R7000 – Porting Xen
Xen output files are distributed in folders –
  /boot
  /etc
  /usr
Problem 1: Xen can’t be added to router firmware directly
  Because it has a read-only filesystem
Solution –
  Re-compile DD-WRT from source along with Xen
    Requires a steeper learning curve to compile DD-WRT
  Or use firmware-mod-kit to extract, modify and rebuild firmware image
    Simple and elegant way to modify firmware binary

## Slide 13: Netgear R7000 – Flashing steps
Setup static IP on host
Start TFTP server on host
While booting, press ctrl-C to exit to CFE console
Pull image from TFTP server and flash
  flash 192.168.1.104:output-firmware.bin flash0.trx

## Slide 14: Netgear R7000 – Bootloader CRC check
Problem 2: CFE in DD-WRT does a CRC check for the authenticity of the image before flashing it
  This prevents Man-In-The-Middle (MITM) attack by which an adversary can display his firmware as an authentic DD-WRT firmware to a naïve user
Solution –
  Modify CFE to circumvent CRC check & re-flash
Problem 3: Modified CFE skipped the CRC check, but failed in the next step because of invalid header in the binary
Solution –
  Understand why this is happening and fix the header
  Use a different binary format
    flash tool accepts .trx and .chk formats apart from .bin

## Slide 15: Alternative hardware – Raspberry Pi
Why Raspberry Pi-3 a good choice ?
  Meant for development environment, so no proprietary software
  Specification
    CPU -
      1.2 GHz 64bit quad core ARMv8
      Supports hardware virtualization
    Memory – 1GB
  Simple to bring up Debian OS on Pi
    On the plus side, Debian supports Xen out-of-the-box
Unfortunately, we had a Raspberry Pi-2 with ARMv6
  With no hardware virtualization and far inferior specification

## Slide 16: Inference
Achieving type-1 virtualization on a commercial router –
  Problems & possible solutions –
    A lot of proprietary software to deal with
      Fortunately, in the course of this project, we’ve solved most of these problems and very close to getting Xen on Netgear R7000 router
    Little (and confusing) documentation on how to flash the hardware or bootloader
      OpenWRT & DD-WRT development forums for the rescue. However, you still need a lot of time to go through all the ill maintained documents and posts

## Slide 17: Inference contd.
Achieving type-1 virtualization on a commercial router –
  Problems & possible solutions contd. –
    Adapting Xen to the hardware is difficult
      One of the first problem we encountered was - no device tree in DD-WRT. This complicates Xen’s work in understanding the underlying hardware
      We’re guessing we would run into more such problems
    Very difficult to port generic OS like Debian or Arch Linux because of hardware driver mismatch
      If we could achieve this, Debian or Arch Linux support Xen out-of-the-box

## Slide 18: Project Source and Documentation
https://bitbucket.org/SavanUA/virtual_router/
Documentation

## Slide 19: Useful links
Xen Project Overview
OpenWRT - Netgear R7000 instructions
Xen ARM
Xen ARM Cross-compiling
Serial console wiki
Devicetree
Porting Xen on a new SOC
How to de-brick your Netgear R7000 router
DD-WRT development and firmware-mod-kit
CFE bootloader documentation

## Slide 20: Reference
Egi, Norbert, et al. "Evaluating xen for router virtualization." Computer Communications and Networks, 2007. ICCCN 2007. Proceedings of 16th International Conference on. IEEE, 2007.
Anhalt, Fabienne, and Pascale Primet. Analysis and evaluation of a XEN based virtual router. Diss. INRIA, 2008.
Fernandes, Natalia C., et al. "Virtual networks: Isolation, performance, and trends." Annals of telecommunications-annales des télécommunications 66.5-6 (2011): 339-355.
Barham, Paul, et al. "Xen and the art of virtualization." ACM SIGOPS Operating Systems Review. Vol. 37. No. 5. ACM, 2003.
Bourguiba, Manel, Kamel Haddadou, and Guy Pujolle. "Evaluating and enhancing xen-based virtual routers to support real-time applications." 2010 7th IEEE Consumer Communications and Networking Conference. IEEE, 2010.
Bourguiba, Manel, Kamel Haddadou, and Guy Pujolle. "Evaluating Xen-based virtual routers performance." International Journal of Communication Networks and Distributed Systems 6.3 (2011): 268-282.